## Slide 1: Hidden Terminal Problem and Exposed Terminal Problem in Wireless MAC Protocols

## Slide 3: Networking basics
Medium Access
Control (MAC)
Protocol
Notes: The Open Systems Interconnection (OSI) model is a product of the Open Systems Interconnection effort at the International Organization for Standardization (ISO).

## Slide 4: Characteristics of Wireless Networks
Multiplexing: in a mobile and wireless network, the wireless medium is shared by many nodes.
Hence, multiple use of a shared medium is a major challenge in wireless networking.
Most decisions for accessing the wireless medium is made in the MAC layer.

## Slide 5: Multiplexing
The wireless channels can be multiplexed in four dimensions:
  Time(t): A channel gets the whole frequency spectrum for a certain amount of time.
  Space(s): Same frequency can be reused when the base stations are separated in space.
  Frequency(f): The whole spectrum is separated into smaller frequency bands.
  Code(c):Each channel uses a unique code for transmitting.

## Slide 6: Time Division Multiplex (TDM)
A channel gets the whole frequency spectrum for a certain amount of time.
Only one user for the medium at a time.
Usually the throughput is high even with many users.
However, no two users should use the medium at the same time. Precise synchronization is needed.
t
f

## Slide 7: Space multiplexing : Cellular Networks
Same frequency can be reused when the base stations are separated in space.
The reuse of frequencies depend on signal propagation range.
Example : fixed frequency assignment for reuse with distance 2.

## Slide 8: Frequency Division Multiplex (FDM)
The whole spectrum is separated into smaller frequency bands.
A band is allocated to a channel for the whole time.
This is somewhat inflexible if the traffic is non-uniform.
An example is radio or TV broadcast. The bandwidth is wasted if a station is off the air.
t
f

## Slide 9: Code Division Multiplex (CDM)
Each channel uses a unique code for transmitting.
All channels use the same frequency spectrum at the same time.
However, signal regeneration is very complex and requires complex HW/SW support.
f
t
c

## Slide 10: Code Division Multiplexing
CDMA has ben adopted for the 3G mobile phone technology.
CDMA is not very suitable for ad hoc networking as we cannot expect specialized hardware/software support at the nodes.
TDMA and its variations are most suitable for ad hoc networking.

## Slide 11: An example of Time Division Multiplexing
CSMA/CD: Carrier Sense Multiple Access with Collision Detection
When a node wants to broadcast, it checks whether any other node is broadcasting (senses the carrier).
A node broadcasts when no other node is broadcasting. Otherwise, it tries later at a random interval.

## Slide 12: CSMA Problems in Wireless Medium
Collision detection is easy in wired networks but difficult in wireless medium.
Collision avoidance to reduce wasted transmissions
S
Transmission
Range of S
R

## Slide 13: CSMA Problems in Wireless Medium
With only one antenna/radio, nodes can only listen or send.
Full duplex radios are extremely expensive.
CSMA gives rise to hidden terminal and exposed terminal problems.

## Slide 14: Message Loss due to Collision
Using CSMA in wireless medium results in message loss and requires retransmission of lost messages.
A node spends much more energy while receiving or transmitting messages. Hence, retransmission wastes a lot of energy.

## Slide 15: Hidden Terminal Problem
R
S2
S1
  Other senders’ information are hidden from the current sender, so that transmissions at the same receiver cause collisions.

## Slide 16: MACA – Multiple Access Collision Avoidance
Use of additional signaling packets
  Sender asks receiver whether it is able to receive a transmission - Request to Send (RTS)
  Receiver agrees, sends out a Clear to Send (CTS)
  Sender sends, receiver Acknowledgements (ACKs)
S1
R
S2
RTS
CTS
ACK
DATA
time
R
S2
S1
1
2
3
4
Detect
Collision
Find Transmission
Complete

## Slide 17: Exposed Terminal Problem
R1
S1
S2
R2
    The sender mistakenly think the medium is in use, so that it unnecessarily defers the transmission.
RTS
CTS
DATA
R1
time
S1
S2
R2
Find medium in use
1
2
3
Wait until medium is clear

## Slide 18: MACA – continued
Exposed Terminal
When a node hears an RTS from a neighboring node, but not the corresponding CTS, that node can deduce that it is an exposed terminal and is permitted to transmit to other neighboring nodes.
R1
R2
S1
S2
RTS
CTS
DATA
S2
R1
time
S1
R2
RTS
CTS
t1
t2
t3
t4
t5
t6
DATA
1
2
3
4
5
6
S2

## Slide 19: MACA – continued
Collision handling
  If a packet is lost (collision), the node back off for a random time interval before retrying

## Slide 20: Quiz
N2
N3
N1
If N1  N2, can N3  N2 simultaneously?
Why this situation happens in wireless network?
How to solve it?
N2
N3
N1
S1
R
S2
RTS
CTS
ACK
DATA
1
2
3
4
time

## Slide 21: Quiz
If N2  N1, can N3  N4 simultaneously?
Why RTS/CTS mechanism do not allow N3  N4?
How to solve it?
N1
N4
N2
N3
N1
N4
N2
N3
RTS
CTS
DATA
S2
R1
time
S1
R2
RTS
CTS
t1
t2
t3
t4
t5
t6
DATA
1
2
3
4
5
6
S2

## Slide 22: Quiz
Is there any collision happens?
What kind of problem (hidden/exposed) shown in the figure?
Node 1
Node 2
Node 3
Node 4
RTS
CTS
DATA
CTS
RTS
time
RTS
N1
N4
N2
N3

## Slide 23: Quiz
Node 1
Node 2
Node 3
Node 4
RTS
CTS
DATA
CTS
time
RTS
DATA
N1
N4
N2
N3
If N1  N2, can N3  N4?
How to solve the problem?

## Slide 24: Summary
Hidden Terminal Problem
  Other senders’ information are hidden from the current sender, so that transmissions at the same receiver cause collisions.
Exposed Terminal Problem
  The sender mistakenly think the medium is in use, so that it unnecessarily defers the transmission.

## Slide 25: Conclusions
A Perfect MAC Protocol
  Collision avoidance to reduce wasted transmissions
    Cope with hidden terminal problems
    Allow exposed terminals to talk
  Reasonable fairness
No MAC protocol does all this!